## Slide 1: Advanced Structure and Plasma Based Particle Accelerators
Colloquium, Fermi National Accelerator Laboratory, June 17, 2015
Notes: Walton and Cockroft (1929, 300kV); Ernest Orlando Lawrence’s 27-inch cyclotron (“proton merry-go-around”, 1931); Donald Kerst’s electron betatron (1941);
Alternative Gradient Synchrotron (AGS) at Brookhaven (33GeV protons, 1960); Fermi Lab’s Tevatron; ILC (??)

## Slide 2: History of Accelerators: Higher Energies from Bright Ideas
“Fermi predicted that future accelerators would grow in power and size. They would not be built on the earth but around it, and physics laboratories would be in outer space… You may expect that at some future time accelerators will change the aspect of the earth and make it resemble the planet Saturn”, Laura Fermi, 1974.
Prediction: 20 TeV CM energy by 1994 at a cost of $170B
NB: SSC would have been 40 TeV CM if it was not cancelled in 1993 (!!)
“What can we learn with High-Energy Accelerators”, Retiring Presidential Address of APS, Columbia, 1954

## Slide 3: How to shorten an accelerator?
Tevatron: 1 TeV/7km proton/antiproton
Huge radius for high energy hadrons and reasonable magnetic field strength:
Rings don’t work for high energy e-p  need linacs
Major problem: synchrotron radiation
LHC: 7 TeV/27km proton-proton

## Slide 4: Shorter Linacs With Higher Accelerating Gradients
SLC 2-mile linac: 50 Gev x 50 GeV collider with L = 1030 cm-2 sec-1
Conventional linacs are very long: 30km for 500 GeV
Accelerating gradient in SC cavities: 32 MV/m
High gradient acceleration enables miniaturization

## Slide 5: High accelerating gradients require high frequencies
Etrap = 10 MeV/m x f [GHz]
Highest frequency possible  laser driven advanced linear accelerators
Credit: David Whittum

## Slide 6: The Basics of Laser Acceleration
Linear in electric field acceleration in vacuum is impossible (Lawson-Woodward-Palmer’s theorem)
Slow electron
photon
Fast electron
Cannot stop a photon in vacuum!
Near-field accelerators: possess non-radiative field components due to boundaries (inverse Smith Purcell, PBG, surface wave, plasma wakefield, …)
Far-field accelerators: electrons execute transverse motion in external DC fields (IFEL, inverse CARM, inverse Ion Channel Laser)
??

## Slide 7: Near-field accelerators
Require boundaries (e.g. apertures in disc-loaded cavities) or a medium supporting non-radiative EM modes (Laser Wakefield Accelerator)
λ= 800 nm
e-beam
laser
T. Tajima & J. M. Dawson, PRL‘79
E. A. Peralta et. al., Nature 503, 91 (2013)

## Slide 8: Far-field Accelerators
Far-field accelerators (no boundaries, plasmas, etc):
Inverse free-electron laser (IFEL):
Cyclotron resonance laser accelerator:
Inverse ion-channel laser (a.k.a. DLA):
Drawbacks: (a) accelerating gradient reduces with , (b) large transverse undulating motion, (c) difficult to maintain resonance condition
IFEL curse

## Slide 9: Outline of the Talk
Need for advanced laser-driven accelerators
Plasma based accelerators at ultra-relativistic laser intensities
  Blowing a plasma bubble: accelerating cavities at the speed of light
  Injecting into a plasma bubble
  The ultimate bubble at the Texas Petawatt
  Direct Laser Acceleration in a bubble
Surface Wave Accelerator Based on SiC
Challenges and Opportunities
B. Neuner III, D. Korobkin, G. Ferro, and G. Shvets, PRSTAB 15, 031302 (2012)
X. Zhang, V. Khudik, and G. Shvets, PRL 114, 184801 (2015)
X. Wang et. al. (Ditmire, Shvets, Downer), Nature Comm. 4, 1988 (2013)

## Slide 10: How Advanced Accelerators Benefit from Plasma?
Plasma Accelerator:
  Disposable
  No breakdown
  No structure fabrication
  High frequency  high fields
  No need for external injectors  plenty of electrons in the plasma (?!)
Example: n0=1018cm-3 eE = 100 GeV/m
In traditional (metallic) structures frequency is determined by feature size. In plasma – by its density.

## Slide 11: Ultimate nonlinear wake: bubble
deceleration
acceleration
Plasma transversely expelled by the ponderomotive pressure of the laser
Plasma-free bubble forms
sheath
Peak acceleration field can considerably exceed the non-relativistic wavebreaking limit
Focusing throughout the bubble  promising “immersion cathode”

## Slide 12: Beyond Wave-breaking Limit: The Bubble
Wei Lu et. al., PRL’06; M. Tzoufras et. al., PoP ‘09.
for
Fields inside a large bubble can considerably exceed the cold wave-breaking limit:
Idealized spherical bubble:
Ponderomotive force of laser expels plasma electrons, balances Coulomb attraction of the ions:

## Slide 13: Plasma is an electron injector
Plasma can be used as a cathode  no need for external injectors  works for both LWFA and PWA
Injection from ambient plasma needs to be understood if you want to avoid it  dark current prevention in externally-injected plasma accelerators
Second pulse injection: O. Lundh et.al. (LOA team), Nature Phys. ‘11
Tunnel ionization of inner-shell electrons inside the wake for injection: A. Pak et. al., PRL’10
Use plasma density gradients: C. G. R. Geddes et. al., PRL ’08; K. Schmid et. al. PRSTAB’10

## Slide 14: Self-injection from plasma into the bubble
Ultra-relativistic (g0 > 100) bubbles  electrons flow around the bubble
What if the bubble is allowed to evolve (expand or shrink)? Injection from plasma!
Electron sheath around the bubble trapping!
Parameters: P=1.33 PW, l=1.054 m, T=150 fs, r=80 m, n=2.51017 cm-3
Normalized: a=3.3, kpr0=7.5, peL=4.23, P/Pcr=19
intensity
S. Kalmykov et. al. PRL 103, 135004 (2009); S.A.Yi et. al., Plasma Phys. Cont. Fusion 53, 014012 (2010)

## Slide 15: Generation of mono-energetic beams: bubble expansion followed by stabilization
x = 2mm: energy spread
x = 5mm
x = 2mm
x = 5mm
phase space rotation
monochromatic beam emerges
The beam becomes mono-energetic due to bubble expansion up to x=3mm  earlier injected electrons experience weaker field  phase space rotation
x = 2mm
x = 5mm
late injection
early injection

## Slide 16
Self-injection and acceleration of mono-energetic 2 GeV electrons at the Texas PW (experiment: M. Downer and the PW Team)
X. Wang et. al. (Ditmire, Shvets, Downer), Nature Communications 4, 1988 (2013)

## Slide 17: Self-Injected 2-GeV Electrons on TPW: Experimental Results
When are electrons injected? Through what mechanism? Why are X-rays generated towards the end of the gas cell? What was the accelerating gradient?
Pieces of the puzzle:
Relatively low energy:
X-rays generated towards in the final 1-2cm of the plasma cell
Self-injection (no dopants)

## Slide 18: Self-Focusing of the TPW: Modeling
Beam’s shape matters: Gaussian vs super-Gaussian
SG beams develop a Airy-like rings early on  late and rapid focusing  bubble formation and injection
The actual amplitude/phase of the beam are unknown
Topological changes due to nonlinear self-focusing is possible: from multiple hot spots to central peak
Low-power profile

## Slide 19: Self-Injected 2-GeV Electrons on TPW: Theoretical Modeling
Rapid evolution of the bubble results in the main injection at followed by a second injection at
Peak accelerating field roughly in agreement with the bubble accelerating field
Electrons accelerated during the final centimeter of the plasma  considerable room for improvement!
X. Wang et. al. (Ditmire, Shvets, Downer), Nature Comm. 4, 1988 (2013)

## Slide 20: Hybrid Laser Wakefield/Direct Laser Acceleration
Combine far-field and laser-wakefield acceleration mechanisms to mitigate slippage between ultra-relativistic electrons and the plasma bubble  more energy from wake, some energy from laser!
X. Zhang, V. Khudik, and G. Shvets, Phys. Rev. Lett. 114, 184801 (2015)

## Slide 21: DLA History: From Plasma Channels…
D. H. Whittum et. al., PRL’90; Phys. Plasmas ‘92
Dave Whittum, Andy Sessler, and John Dawson invent an ion channel laser
A. Pukhov et. al., PoP’99; C. Gahn et. al., PRL’99
The MPQ team proposes and realizes the inverse ion channel laser

## Slide 22: …to Plasma Bubbles!
A great deal of theoretical work: Nemeth, et al., PRL’07, PRL; Phuoc, et al., PoP’08, J. L. Shaw et. al., PPCF’14
Dino Jaroszynski produces MeV Gamma rays, possibly via DLA mechanism inside a bubble!! S. Cipiccia et. al., Nature Physics’2011
“In fact, this observation of high harmonic generation could provide the first (albeit somewhat indirect) experimental evidence of DLA, which has so far been elusive.” G. Shvets, Nature Physics’2011
Big questions: (a) monochromatic beam? (b) best laser pulse format? (c) best injection approach? (d) major paradigm shift of LPAs in the making??

## Slide 23: Ultra-relativistic DLA: PIC Simulations
Pump pulse creates a bubble
Electrons are self-injected and interact with weaker laser pulse delayed by Dt=80fs
Electrons naturally separated into two groups electrons with large gain more energy
Density bump “shakes” the bubble  side-injection with large  enables DLA
Pump: ,
Trailing Probe: ,
L2 =1.6mm, L3 = L4 = L5
I0=2×1019w/cm2; I1=4×1018w/cm2
n0=1.8×1018cm-3; n1=5.4×1018cm-3
delay:80fs
after 1cm propagation

## Slide 24
2D PIC simulation of DLA/LWFA
Strong phase space bifurcation  high-energy DLA electrons are spatially separated from lower-energy non-DLA electrons
Two-peak energy distribution separated by 400 MeV
Bifurcation is absent when the DLA pulse is absent
with DLA pulse
w/o DLA pulse
DLA
non-DLA
Notes: first introduce three plots and one gif.

## Slide 25
Synergistic Laser Wakefield/Direct Laser Acceleration: Dephasing Suppression
DLA
non-DLA
DLA electrons  strong correlation between total energy and transverse energy
Strong bifurcation in phase space
Synergy between DLA and LWFA  higher energy gain from the wake for the DLA population  delayed dephasing!
DLA electrons gain extra 200 MeV from the wake and extra 400MeV from the laser (DLA)
X. Zhang et. al. PRL 114, 184801 (2015)
Notes: first introduce three plots and one gif.

## Slide 26: Laser Accelerates, Wake Decelerates?
pulse:
TW ()
fs, m
The wake decelerates the electrons, but the DLA accelerates them at more than twice the deceleration rate!
What about the “IFEL curse”: ?
Loss to wake
Gain from laser
External injection into the decelerating phase
Deceleration phase

## Slide 27: One Step Back, Two Steps Forward: Constant Gradient Direct Laser Acceleration
Transverse energy growth
Model: constant decelerating field
Multiple DLA harmonics:
,
Initial conditions

## Slide 28: How the entire LPA paradigm may be changed by Direct Laser Acceleration
Synchronization of externally injected beam is the key to injecting into the decelerating phase
The main role of the bubble is not accelerate but to provide focusing field to undulating electrons
Excellent source of X-ray and Gamma-ray radiation because of the large undulator parameter

## Slide 29: Surface Wave Accelerator and Radiation Source Based on Silicon Carbide
B. Neuner III, D. Korobkin, G. Ferro, and G. Shvets, PRSTAB 15, 031302 (2012).

## Slide 30: Wakes at the double interface
Supports w = kc mode  can accelerate relativistic particles
Almost like a hollow channel PWA, except there is no plasma: optical phonons!
Can be used as a Surface Wave Accelerator Based on SiC (SWABSiC), or
Diagnostics for ultra-short bunches  Coherent Surface Cherenkov Radiation
SiC/vacuum SPP’s are excitable by either short bunches and bunch trains (“PWA”) or by a CO2 laser (direct acceleration)
z
x
10 mm

## Slide 31: Modes Supported by SWABSiC
Accelerating (longitudinal) mode
SiC
SiC
SiC
SiC
Deflecting (transverse) mode
6 mm
Phase velocity of the mode:
Super-luminous modes cannot interact with beam
Sub-luminous modes propagate at finite angle with beam (“Cherenkov modes”)
Direct laser excitation  through a prism because the gap is too narrow
Super Luminous
SubLuminous

## Slide 32: SWABSiC fabrication: SiC-on-Si growth
Si “brick”
Step 1: Grow 1.7 mm of SiC
Step 2: Spin-coating of 10 µm of PMMA (photoresist) and development/patterning
Step 3: Final Assembly
6 µm gap
Accelerator in a pocket…
But not in a wafer holder!

## Slide 33: Optical Characterization of SWABSiC
From Laser
Reflected Beam
Refracted Beam
To Power meter or IR camera
Si
Si
SiC
SiC

## Slide 34: Beam-Driven Wake in SWABSiC
Cherenkov Surface Wake can be excited either by a single short (<30fs) bunch, or by a micro-bunched beam
Can be diagnozed either optically or through energy gain/loss
x
y
q
Cherenkov Wake in SWABSiC
y
x
z
Vb
To IR camera
Si
Si
To spectrometer

## Slide 35: Outline of the Talk
Need for advanced laser-driven accelerators
Plasma based accelerators at ultra-relativistic laser intensities
  Blowing a plasma bubble: accelerating cavities at the speed of light
  Injecting into a plasma bubble
  The ultimate bubble at the Texas Petawatt
  Direct Laser Acceleration in a bubble
Surface Wave Accelerator Based on SiC
Challenges and Opportunities
B. Neuner III, D. Korobkin, G. Ferro, and G. Shvets, PRSTAB 15, 031302 (2012)
X. Zhang, V. Khudik, and G. Shvets, PRL 114, 184801 (2015)
X. Wang et. al. (Ditmire, Shvets, Downer), Nature Comm. 4, 1988 (2013)

## Slide 36: Acknowledgements
Postdocs/Staff:
Vladimir Khudik Dmitriy Korobkin Simeon Trendafilov
PhD Students
Kueifu Lai Xi Zhang Burton Neuner Austin Yi

## Slide 37: Meet our group!
Postdocs & Research Staff:
S. Trendafilov (plasma: theory) V. Khudik (plasma: theory) A. Khanikaev (photonics: th)
PhD Students:
Y. Urzhumov (Russia)  ’08 B. Neuner III (USA) PhD’11 C. Fietz (USA)PhD’11 H. Moussavi (Iran)PhD’12 C. Wu (Taiwan)PhD’12 Nima Dabidian (Iran) Austin Yi (USA) PhD’12 Nihal Arju (India) Glen Kelp (Estonia) Kueifu Lai (Taiwan) Xi Zhang (PRC) Carl Siemon (USA) Tzuhsuan Ma (Taiwan)

## Slide 38: SWABSiC Fabrication
Step 1: cutting Si discs (D=5cm, t=5mm) into 22x12x5 mm slabs
Step 2: growth of 1.7 mm SiC in Lyon, France
Step 3: cutting Si slabs into prisms (ISP Optics)
28º angle
15º angle
1.78 mm
10 mm
20 mm

## Slide 39: Laser-excited wakes for many wavelengths
Accelerating wake
Deflecting wake
Both accelerating (good) and deflecting (parasitic) wakes are experimentally observed
The focus at will be beam-driven wakes
Wakes must be sub-luminal to be excited by the bunch
l = 11.310 mm
l = 11.128 mm
l = 11.065 mm
l = 10.850 mm
l = 10.784 mm
l = 10.723 mm