## Slide 1: The CDF Experiment, and the Italians
The start of the US-Japan-Italy Collaboration
The construction of the run1 detector
The discovery
The powerful run2 detector
The wealth of great physics
The legacy
Giorgio Bellettini, Fermilab Colloquium
May 3, 2017

## Slide 2: Frascati-Pisa, the first Italian groups in CDF
In September 1979 at the Electron-Photon conference in Fermilab, Paolo Giromini and I decided to put together two groups for an experiment at the Tevatron collider which was being built.
In December I met at CERN with Alvin Tollestrup and Robert Diebold and proposed to establish a USA-Japan-Italian collaboration to design and operate a magnetic detector at the Tevatron. An agreement between the US and a Japanese group lead by Kunitaka Kondo existed already. The extension to Italy was readily accepted in the US.
By Spring 1980 INFN approved the initiative and two strong Frascati-Pisa groups were in place.

## Slide 3: CDF milestones
1981: the detector Design Report
1) 1985: Collisions at 1.6 TeV observed with the calorimeters
2) 1988-1989: ≈ 4 pb-1 Commissioning run at √s = 1.8 TeV
3) 1991-1996: “Run 1” ≈ 110 pb-1 on tape at √s = 1.8 TeV
4) 2001-2011: “Run II” at √s = 1.96 TeV, ≈ 10 fb-1 on tape

## Slide 4: The Institutions in the 1981 CDF design report
Argonne,
Chicago,
Fermilab,
Harvard,
Illinois,
LBL,
Purdue,
Texas A&M,
Wisconsin
CDF was born as a
USA-Japan-Italy endeavor
13 Institutions
87 physicists
56 Americans, 15 Japanese , 16 Italians
KEK
Tsukuba
Frascati,
Pisa
US
Japan
Italy

## Slide 5: 24 events in 1985, and Stefano Miscetti`s Thesis
Tevatron demonstration run in 1985 (at 1600 GeV)

## Slide 6: CDF1 detector

## Slide 7: CDF1 parts of primary Italian design
1) Small angle spectrometers to measure σtot
2) Projective towers of plastic scintillator in the central hadronic calorimeter.
3) The silicon vertex detector SVX around the beam pipe.

## Slide 8: The CDF small angle spectrometers
Unique measurements at the highest p-pbar energies:
1) Total cross section
2) Elastic scattering
3) Single diffraction

## Slide 9: The CDF1 small angle detectors
The momentum of the forward scattered primary could be measured on the antiproton side.
Two intermediate angle telescopes measured the inelastic rate.
Paolo Giromini was the leader of the Frascati small angle chamber project.
The Pisa group under Guido Tonelli and Giorgio Apollinari were in charge of the silicon detectors.

## Slide 10: First Physics in 1988
Measurements were made at
√s = 548 and 1800 GeV. The cross section increase with energy discovered at the ISR in p-p was confirmed in p-pbar.

## Slide 11: INFN contributions to the hadron calorimeters (a Fermilab-Purdue-INFN project)
Scintillators, light guides, phototubes, power supplies, laser flasher of the barrel and endwall hadron calorimeter: the sensitive components of 50 barrel and endwall hadron wedges were designed, built and run-in by the Italians.
In 1981-1982 the INFN hardware was moved to Fermilab in 11 ship containers.

## Slide 12: Light guide fabrication in Frascati
The Frascati Group lead by Paolo Giromini gave a major contribution to the central calorimeter.
Sergio Bertolucci was in charge of the light guide construction.
The readout BBQ bars were fabricated in Pisa

## Slide 13: Light guides installed in the central wedge

## Slide 14: Young Italians assembling the wedges

## Slide 15: The superconduting coil came from Japan

## Slide 16: The roman arches of the central calorimeter
Hans Kautsky proved in person that the arches were self-supporting.

## Slide 17: The central CDF1 detector
In 1985 the three national flags were displayed on top of the central detector in the assembly hall.
Japan USA Italy

## Slide 18: Hadron jets in the CDF calorimeter
Mjj = 1364 GeV
EM calorimeter energy
Hadronic calorimeter energy
ET = 666 GeV
ET = 633 GeV
  r-f view
η vs. φ

## Slide 19: The Silicon Vertex Detector proposed by the Italians
The SVX concept in the 1981 Design Report

## Slide 20: The role of Aldo Menzione
Leader of the Italian campaign to establish the potential of precision tracking with silicon detectors at hadron colliders.
In charge of design, construction and commissioning of the CDF1 silicon vertex detector
Panofsky price in 2009 with Luciano Ristori.

## Slide 21: SVX1 (built with Fermilab and LBL)
Proposed in 1981, Approved in 1988,
Operating in 1991
½ of SVX1 is saved in the Pisa University museum.

## Slide 22: The discovery

## Slide 23: 10 years of lower limits to the top quark mass (95% c.l.)
PETRA/PEP > 22 GeV/c2 in 1984
TRISTAN > 26 GeV/c2 in 1988
SLC > 41 GeV/c2 in 1989
LEP > 45 GeV/c2 in 1989
UA1 > 50 GeV/c2 in 1990
UA2 > 69 GeV/c2 in 1990
CDF > 70 GeV/c2 in 1990
UA2 and CDF > 77 GeV/c2 in 1991

## Slide 24: The UA1 top quark kinematic search (Mtop < MW )
UA1 had built a probability parameter from the transverse momenta of known jet production processes, relative to the values expected from the decay of a heavy top quark:
QCD
Top 80 GeV/c²
A top quark of about 80 GeV would have been above threshold at the SPS.

## Slide 25: t-tbar events at the Tevatron for Mtop > MW

## Slide 26: CDF kinematic search for a heavy top (a` la UA1)
Radiated QCD jets have mostly low Et
Decay prongs of slow-moving heavy objects can have larger Et
The heavier the top quark, the greater the excess of large Et jets.

## Slide 27: Relative likelihood in single lepton candidate events (summer 1993)
MONTECARLO
DATA
The Pisa group (Hans Grassmann, et al.) simulated the distributions of large transverse energy jets in known W+jets events and in t-tbar events, and found evidence in the data for a contribution of top-like events

## Slide 28: The powerful SVX : Top pair candidate, 1994
Tagging efficiency of b-jet pairs in t-tbar events ≈ 42%
Tagging efficiency of light quark energetic jets ≈ 0.5%.
Candidate

## Slide 29: Secondary vertices in the 1994 Evidence Paper
Including single and dilepton channels, 15 top-like tags were found against 5.9 expected.
This corresponded to a 2.8 σ fluctuation.
Single lepton sample

## Slide 30: Top quark mass in the Evidence Paper
7 single lepton events could be reconstructed to find the mass. A peak was found at mt = 174 ± 17 GeV/c2.

## Slide 31: Discovery of the top quark in 1995

## Slide 32: Italians in the top quark discovery
Italians in the top discovery
BOLOGNA 8
FRASCATI 5
PADOVA 11
PISA 36
60 Italian authors, ~13% of the CDF Collaboration.
In 1995 a Swiss group (Geneva) was the only other European group in CDF.

## Slide 33: The growth of the CDF Collaboration
After the top quark discovery many European groups from Germany, Finland, Russia, United Kingdom, Spain, joined CDF for Run II.
Many non-European Institutions also joined from Canada, Japan, Korea, Taiwan (in 1993)

## Slide 34: The increasing Italian participation
1980, Frascati and Pisa
1990, Padova
1992, Bologna
1997, Trieste-Udine
1999, Rome
Discovery of the top quark (1995)
Start of Run 2 (2001)

## Slide 35: The Italian summer students
In 1983 the Pisa group started a summer student program by hosting three physics students for a few months at the lab to help in the experiment. At present, the program is still run by former CDF Italians but has expanded greatly beyond CDF, growing up to 36 students in 2016. It involves physics and engineering students to be trained in science and technology in all groups of Fermilab.
The Italian summer students program has contributed significantly to lab science. Several former students are now staff members, even in leadership positions in the lab management.

## Slide 36: CDF in run2
Remaining from Run1:
the solenoid
the central calorimeter
a fraction of the muon detector
New
the tracker
  SVX2 and ISL
  The central drift chamber COT
the forward calorimeter plugs
the extended muon detector
The time of flight counters
the front-end electronics
the trigger/DAQ electronics
A major effort. The detector was extensively rebuilt.
Bob Kephart and Cathy Newman-Holmes project leaders

## Slide 37: Italians in the CDF2 Design Report (1993)
Bologna, Frascati, Padova, Pisa
63 authors out of 389

## Slide 38: The largest Italian contingent (April 2003)
53 CDF groups, about 650 physicists
6 Italian groups, 111 physicists
Bologna: 10 physicists
Frascati: 7
Padova: 22
Pisa: 37
Rome: 21
Trieste/Udine: 14

## Slide 39: Italian contributions to the CDF2 detector
The secondary vertex tracker (Pisa-Chicago-LBL)
The Intermediate Silicon Layers (Pisa-Tsukuba-Fermilab)
The laser flasher of the scintillator plug calorimeter (Udine)
The upgraded muon scintillation detectors (Pisa-JINR)

## Slide 40: The plug calorimeters
Towers of plastic scintillators, as in the central calorimeter.
Calorimeter coverage was extended to abs = 3.6.

## Slide 41: The time of flight counters
The TOF counters were laying on the inner surface of the solenoid

## Slide 42: The CDF2 tracker

## Slide 43: SVX2
The ~ 100 cm long, second generation SVX2 contained 5 layers of double-side sensors, within 8 cm from the beam axis.

## Slide 44: ISL
The ISL construction in Pisa was lead by Giorgio Chiarelli

## Slide 45: Central Outer Chamber “COT” ”the hart of CDF”
A Fermilab project
96 wire planes
  30,240 signal wires
  Four z- and four 3º-stereo superlayers,
  0.88 cm wide cells with drift time 100 ns

## Slide 46: A counter of the outer muon detector (a JINR contribution)

## Slide 47: SVT electronics
The electronics of the secondary vertex tracker was a specialized sector of the run2 trigger

## Slide 48: Secondary vertex tracker SVT
Fast electronics (XFT) feeds segments of COT tracks to SVT
Associative memory combines them with hits in the SVX and finds tracks which are not likely to come from the primary vertex
Tracks are found in ~20 μs. Triggering at level 2 becomes possible on hadronic Charm and Beauty decays.

## Slide 49: The role of Luciano Ristori
Luciano conceived and proposed to the CDF Collaboration in 1990 an addition to the trigger electronics capable to trigger on secondary vertexes (SVT).
The SVT trigger has made accessible to CDF measurements otherwise impossible at a hadron collider, in the area of hadronic decays of B mesons and baryons, including a precise measurement of the Bs oscillation frequency.
Panofsky price with Aldo Menzione in 2009.

## Slide 50: The wealth of great physics

## Slide 51: The huge CDF2 physics span
Properties of top quark pair production and decay
Observation of EW production of single top quark
W mass
W, Z single and associated production
Wide field of heavy flavor physics
Single and multi-jets physics
Higgs boson search…
Many results will stay forever in the Physics books

## Slide 52: W mass February 2012
MW = 80387 ± 19 MeV/c2 ( ± 12 (stat.) ± 15 (syst.))
ppbar  WX  eγX

## Slide 53: Top quark mass winter 2011
All-hadronic
MET+Jets
Dilepton
Constraint from x-sec
Top mass from t-tbar event fitting
Mass of the hadronically decaying top
CDF combination (winter 2011) : mtop = 172.70 ± 0.63(stat) ± 0.8(syst) GeV/c²
Tevatron combination (summer 2011): mtop = 172.2 ± 0.6(stat) ± 0.8(syst) GeV/c²
https://arxiv.org/pdf/1409.4906.pdf
Single lepton
All hadronic

## Slide 54: Bs0 – Bs0 mixing
(PRL 97, 242003 2006)
87 fs (< 30 μm, 0.4%) resolution for fully reconstructed states
5.4 s significance
__

## Slide 55: Another major contribution of Italians at Fermilab (courtesy of Peter Garbincius)
Italian collaborators in the E687-E831 (“FOCUS” ) Charm photoproduction experiment contributed the silicon microstrip vertex detector and readout, which were essential for the experiment.
Bologna: Pierluigi Frabetti.
Frascati: Adriano Zallo, Franco Fabbri, Stefano Bianco
3) Milano: Angela Sala, Daniele Pedrini, Dario Menasce, Donatella Torretta, Gianpaolo Bellini, Laura Perasso, Luigi Moroni, Mariella Di Corato, Margherita Vittone, Sandra Malvezzi, Silvano Sala
4) Pavia: Gianluca Boca, Sergio Ratti.

## Slide 56: Beauty-baryons observed by CDF
last observed

## Slide 57: Evidence for a Higgs boson at the Tevatron (contributed primarily by H → b-bbar)

## Slide 58: 699 published CDF papers (1988-2016)
Also 99 papers published in NIM, with 6168 citations

## Slide 59: Close to 56.000 citations of CDF papers as of April 2017

## Slide 60: 637 Ph.D`s earned with CDF (May 1, 2017)

## Slide 61: 68 Ph.D`s earned by Italians (April 2017)
Pisa 25, Padova 15, Siena 8, Roma 4, Bologna 4, Trieste 3, Trento 2,
Udine 2, Cassino 1, Firenze 1, Milano 1, Pavia 1, Torino 1

## Slide 62: Italian CDF Co-Spokespersons
1995 Giorgio Bellettini
1998-2000 Franco Bedeschi
2002-2004 Luciano Ristori
2010 Giovanni Punzi
2012 Luciano Ristori
2015 Giorgio Bellettini
2017 Giorgio Chiarelli

## Slide 63: The CDF Collaboration in May 2017
389 authors
62 Italians

## Slide 64: The expected CDF legacy measurements MW , Mop will eventually be combined with D0 (and with LHC)
MW : shooting for a total error ≈ 10 MeV
Mop : shooting for a total error ≈ 0.9 GeV/c²
Many other important analyses are ongoing:
1) Search for anomalous heavy hadron states
2) Search for b-bbar resonces in dijets
3) Associated W+jets production
4) Tevatron combination of F/B asymmetry in t-tbar
5) Tevatron combination of F/B asymmetry in DY
6) Top polarization in the dilepton channel
7) t-tbar cross section with full statistics
8) Central exclusive production…

## Slide 65: Final comment
CDF was a great success. Can such a success be repeated?
An excellent accelerator, an excellent detector design, a powerful brain trust. Yes, such a success can be repeated.
A major Italian contribution. This can and must be continued.
3) Great physics was around the corner at the Tevatron. It can happen again.