## Slide 1
Allan Rowe
PIP-II IKC Technical Integration Manager
55th Annual Users Meeting
13-June-2022
PIP-II Project

## Slide 2
Outline
13-June-2022
Motivation & PIP-II Project Overview
PIP-II Project Status & Recent Major Achievements
Near Term Goals & Summary

## Slide 3
PIP-II Project Meets the P5 Report Mandate
Recommendation 13: Form a new international collaboration to design and execute a highly capable Long-Baseline Neutrino Facility (LBNF) hosted by the U.S. To proceed, a project plan and identified resources must exist to meet the minimum requirements in the text. LBNF is the highest priority large project in its timeframe.
Recommendation 14: Upgrade the Fermilab proton accelerator complex to produce higher intensity beams. R&D for the Proton Improvement Plan II (PIP-II) should proceed immediately, followed by construction, to provide proton beams of >1 MW by the time of first operation of the new long-baseline neutrino facility.
13-June-2022

## Slide 4
LBNF / DUNE / PIP-II
Fermilab Complex and PIP-II
Provide 1.2 MW beam power
Batavia, IL
Target (part of LBNF scope )
and Near Detector (part of DUNE scope)
Characterize primary beam
Batavia, IL
Sanford Underground Research Facility -- Lead, SD
Deep Underground Neutrino Experiment (DUNE) (LAr 4 x 10 kt (fiducial mass) detectors)
Located in Underground Caverns (1.5 km) (part of the LBNF scope)
1300 km
13-June-2022

## Slide 5: PIP-II Mission
13-June-2022
PIP-II Capabilities
Beam Power
1.2 MW proton beam
Upgradeable to multi-MW
Flexibility, multi-user capability
CW-compatible
Customized beams
Multi-user delivery
Reliability
Modernizes Fermilab accel complex
PIP-II is an essential upgrade to the Fermilab accelerator complex to enable the world’s most intense beam of neutrinos to LBNF/DUNE and to serve broad physics research program for decades to come.
PIP-II Scope
800 MeV H− SRF linac
  CW RF Operations
Linac-to-Booster transfer line
Accelerator Complex Upgrades
  Booster
  Recycler
  Main Injector
Conventional Facilities
  Space reserved for two CMs for 1 GeV Upgrade
The PIP-II scope enables the accelerator complex to reach 1.2 MW proton beam on LBNF target

## Slide 6
PIP-II will provide highly capable, reliable, upgradeable, and expandable accelerator infrastructure with significant savings to the DOE. TPC = $978MM + $310MM In-kind

## Slide 7: In-kind Contribution Status
All international legally binding agreements are signed and in-place.
Detailed Project Plans are signed with United Kingdom (STFC-UKRI), Italy (INFN), and Poland (WUST).
France (CEA and CNRS) and India (DAE BARC and RRCAT) plans are nearing completion.
May-2021
June-2021
January -2022
13-June-2022

## Slide 8: PIP-II 800 MeV SRF Linac
PIP-II is the first U.S. accelerator project to be built with significant international contributions
8
2.1 MeV
10 MeV
32 MeV
177 MeV
Room Temperature
Superconducting
H- Ion source
RFQ
Cryoplant
2.5kW @ 2K
CDS
Elliptical
LB650 X 9
650 MHz
516 MeV
833 MeV
HWR
162.5 MHz
Single Spoke 1
pSSR1 X 2
325 MHz
Single Spoke 2
SSR2 X 7
325 MHz
Elliptical
HB650 X 4
650 MHz
13-June-2022
RF Amplifiers + RT magnets
Cryoplant is largest single In-kind contribution

## Slide 9
PIP-II Major Milestones
13-June-2022
PIP-II Ground-breaking
Jul 2020 Cryoplant Bldg. Construction Approved

## Slide 10
PIP-II Project Status and Recent Major Achievements
13-June-2022

## Slide 11: Progress in SRF & Cryogenics – PIP-II Cavity Development
Name (Qty.) | HWR (8) | SSR1 (16) | SSR2 (35) | LB650 (36) | HB650 (24) | Units
Type | Half-Wave | Single Spoke | Single Spoke | Elliptical | Elliptical | -
 | 0.11 | 0.22 | 0.47 | 0.61 | 0.92 | -
Frequency | 162.5 | 325 | 325 | 650 | 650 | MHz
Q0 |  |  |  |  |  | -
Gradient | 9.7 | 10 | 11.5 | 16.8 | 18.7 | MV/m
Doped | No | No | No | Yes | Yes | -
Name (Qty.) | HWR (8) | SSR1 (16) | SSR2 (35) | LB650 (36) | HB650 (24) | Units
Type | Half-Wave | Single Spoke | Single Spoke | Elliptical | Elliptical | -
 | 0.11 | 0.22 | 0.47 | 0.61 | 0.92 | -
Frequency | 162.5 | 325 | 325 | 650 | 650 | MHz
Q0 |  |  |  |  |  | -
Gradient | 9.7 | 10 | 11.5 | 16.8 | 18.7 | MV/m
Doped | No | No | No | Yes | Yes | -
Prototypes validated
Prototype in progress
13-June-2022

## Slide 12: Progress in SRF & Cryogenics – PIP-II Cryomodule Development
HWR
SSR1
SSR2
LB650
HB650
5.9 m
5.3 m
6.5 m
9.9 m
5.5 m
Prototypes validated
Pre-Production Cryomodules
Prototype in progress
13-June-2022

## Slide 13: PIP2IT As Testbed for PIP-II Technologies
PIP2IT was a nearly complete PIP-II Warm Front End with the first two cryomodules, HWR and prototype SSR1
  PIP2IT Front End will be stored and reinstalled at PIP-II
PIP-II
13-June-2022

## Slide 14: PIP2IT Tests Successfully Completed
PIP-II design beam parameters demonstrated
Energy = 16 MeV
Pulse beam cur = 2 mA
Pulse length = 550 s
Pulse rep rate = 20 Hz
Chopped beam pattern
Bunch-by-bunch chopping pattern required for LBNF demonstrated
MEBT chopper is critical for PIP-II operations, capable of removing individual bunches, provides arbitrary bunch pattern capability
Critical technologies demonstrated
Beam accelerated to 17 MeV
HWR and SSR1 Prototype cryomodules performance validated with beam
ML algorithm applied successfully to align orbit
Partner deliverables seamlessly integrated
Eight 7 kW amplifiers
SSR1 Cavity
RF MEBT magnets
Radio frequency quadrupole
Half Wave Resonator cryomodule
13-June-2022

## Slide 15
PIP2IT Transition to Cryomodule Test Stand
Infrastructure modifications for the 650 MHz cryomodule test stand are complete, ready for arrival of pHB650 cryomodule
Evolution of PIP2IT Test Facility (same area shown in all) images)
PIP2IT Test Accelerator
(April 2021)
PIP2IT Test Stand
Infrastructure installed
(May 2022)
CAD model of 650 MHz Test Stand with pHB650 cryomodule installed
(Fall 2022)
13-June-2022

## Slide 16: Progress in Accel. Systems
Test area demonstrations
  325 MHz, 650 MHz LLRF/RFPI control
  7 kW, 20 kW 325 MHz amplifiers
  40 kW 650 MHz amplifier
  RF Distribution
  Front end vacuum system
  Room temperature magnets
  Fully EPICs controls
Designs being finalized
  Vacuum systems
  Machine Protection Systems
  Integrated LLRF System
650 MHz, 40 kW SSA
650 MHz LLRF
650 MHz RF Distribution
EPICS user interface
13-June-2022

## Slide 17
All scope downstream of the SRF linac
Designs and Prototyping nearly complete
  Beam Transfer Line and Absorbers
  Specialty Magnets
  Booster RF upgrades
  Main Injector RF upgrades
  Recycler Ring 53 MHz RF cavities
13-June-2022
Booster Gradient Magnets
ORBUMP Magnets
Booster Collimators
Upgraded MI RF
RR Mock-up 53 MHz cavity with tuner
Progress in Accelerator Upgrades

## Slide 18
Cryogenic Plant Building Construction Progress
Authorization for Use and Possession in July 2022
Ribbon cutting - July 11th
13-June-2022
June 2022

## Slide 19
Conventional Facilities Progress
13-June-2022
Site Work Construction Package:
  Construction start in October 2021
  On track for completion in November 2022
Linac Complex (largest PIP-II contract)
  Issued for Proposals in April 2022
  Proposals received on June 7, 2022
Booster Connection
  Design completed
A0 Pond Restoration

## Slide 20
Near term goals & Summary
13-June-2022

## Slide 21
Major PIP-II Milestones to complete in FY2022/23
Complete the Cryoplant Building Construction
Complete Prototype HB650 Cryomodule
Convert PIP2IT to a PIP-II Cryomodule Test Facility
Begin Linac Complex Construction
13-June-2022

## Slide 22
Summary
PIP-II CD-3 is approved. Starting project execution phase with delivery in 2028.
PIP-II will enable the world’s most intense beam of neutrinos to the LBNF/DUNE; modernize Fermilab’s accelerator complex enabling science for decades to come;
PIP-II is breaking new ground as the first DOE/SC accelerator to be built with significant international contributions;
PIP-II International Partnerships are making excellent technical progress by completing designs, demonstrating critical technologies, and beginning project construction;
Strong support from Fermilab, Partners, Physics Community, OHEP, Office of Science, DOE, Congress;
Thanks to the Fermilab Users Community for your support
https://pip2.fnal.gov/
13-June-2022

## Slide 23: Thank You
13-June-2022
Notes: Keep