## Slide 1
AI-on-chip: Microelectronics for enabling data reduction at source
An Engineer’s perspective
Farah Fahim
User’s meeting
June 15, 2022

## Slide 2: Major challenges at HEP detectors
EXTREME RADIATION ENVIRONMENT
E.g. HL LHC: Total ionizing dose : ~ 1 Grad
Single event effects :
Flux of > 20 MeV hadrons = 10 MHz/cm2
Target 1 error every ~10s for 6M channel detector.
Radiation tolerant design and Triple Modular Redundancy for SEE mitigation
DATA VOLUME
On detector data compression of 4 – 15% eventually better than < 1%
OCCUPANCY
LHC: 50 pile up to HL-LHC: 200 pile up
Requires more granular detectors → increasing data volume, power consumption, more complex on-detector electronics

## Slide 3
Why do we need data processing on the edge
POWER: CV2f x (data volume) problem
Total power consumption to move data from pixel to periphery: 1 pJ/bit (~ 5mm distance)
Total power consumption to move data off-chip: > 0.1 nJ/bit
Minimize C,V
3D Integration (high density, low capacitance interconnect)
Low voltage signaling
Reduce data
Typically just zero-suppression for on-detector electronics – OK for sparce data
HL LHC:
Higher granularity, higher occupancy, higher precision
=> needs NEW APPROACH

## Slide 4: Fermilab Microelectronics Capabilities and Mission
ACADEMIC RESEARCH
NATIONAL LABS: ADVANCED SCIENTIFIC INSTRUMENTATION
Support interdisciplinary research
Enables new scientific discovery and foundational engineering
Novel solutions
Mission: new knowledge and education of students
Support scientific experiments operating in extreme environments
Mid-size scaling for large experiments
Mission: robust performance over several decades
INDUSTRY – PRODUCT DRIVEN
Support consumer electronics
Mature designs
Mission: incremental product driven design

## Slide 5: Co-design: Physics – Algorithm – Microelectronics Hardware
Hardware
AI
Physics
Interdisciplinary
Codesign
System on Chip
Resource constrained extreme environment
Physics based distributed AI
Efficiency and Reconfigurability
Heterogenous System in Package
Digital scaling / Mixed signal approach
Integrated non-volatile memory / 3DIC / Wireless (5G)
HL-LHC / XFEL / Synchrotron light sources
CNN / SNN/ Transfer learning/ Distributed AI
Resource constrained environment
  High Radiation
  Limited Power/Material budget
  Where should this intelligence be added ?
Efficiency and reconfigurability
  Ultra-low energy per inference at extremely high rates (10’s ns)
  Reprogram both network and parameters
  On-chip learning / inference
Physics based Algorithms
  Independent events
  Depth vs. classification
  Compression vs. filtering

## Slide 6: Step 1: How to do it? Establish design methodology

## Slide 7: Deep Neural Network: Autoencoder for data-compression
Enable edge compute : Data compression for efficient usage of power and bandwidth
Programmable and Reconfigurable: ability to reprogram weights to adjust for detector conditions and eventually lead to self-learning intelligent detectors
Hardware – Software codesign : Algorithm driven architectural approach
Optimized : Low power and Low latency
Operating in extreme radiation environment: 200 M rad
Autoencoder for data compression is the first use case towards a DNN based on-chip learning and inference
Encoder
Decoder
On-detector ASIC
Reprogrammable weights
Original data
Reconstructed data
Compressed data
- Efficient power and bandwidth usage
reconfigurable
Rate: 40MHz
Work in latent space
Pruned network
Full decoding with mirror weights
Off-detector FPGA

## Slide 8: Physics Driven Hardware Co-design
Algorithm development based on Physics data
hls4ml simplifies the design of on-chip ML accelerators
    | hls4ml directives | << | HLS directives |
    C++ library of ML functionalities optimized for HLS
TMR4sv_hls: Triple Modular Redundancy tool for System Verilog & HLS
Automated Triple Modular redundancy
Notes: We want to present a new paradigm in physics driven hardware co-design for ASICs
We have come up with an entire tool flow to go from algorithm development to ASIC implementation
ML physics algorithm are developed on Keras and Tensor flow by model training
Which then feeds into hls4ml tool – developed by Fermilab & collaborators –
It essentially provides a set of directives to simplify the design of on-chip accelerators
This output feeds into a commercially available High level synthesis tool to generate RTL for digital implementation. We Can implement TMR at this stage along with other RTLs. Finally leading to a layout for manufacture
Next slide please

## Slide 9: HL LHC High Granularity Calorimeter*: Data flow
Fully reconfigurable to adapt to different detector geometries
CNN: Encodes information by correlating spatial features
conv2D layer – extract spatially corelated geometric features
Flatten layer – Vectorizes the 2D image from the conv2D layer [8 x 4 x 4 = 128 x 1]
Dense layer – aggregates the various features to provide higher order information
ReLU – an activation function which introduces non-linearity by applying thresholds (part of both the conv2D and dense layers)
Notes: ReLU – Rectified linear unit

## Slide 10: Rapid design prototyping Neural Network architecture optimization

## Slide 11: 1st AI-on-chip for HEP: ECON Autoencoder
It works as intended !!!
Performance comparable to other expert algorithms
Rad hard with fully triplicated weights immune to Single Event Effects
Successful collaboration with Siemens mentor
Successful demonstration of hls4ml for ASICs

## Slide 12: Step 2: How to reuse and verify? Develop and leverage open source tools

## Slide 13: Embedded Scalable Platform
Accelerator Flow
Simplified design
Automated integration
SoC Flow
Mix & match floorplanning GUI
Rapid FPGA prototyping
Expanded to chip prototyping and verification by emulation
ESP website: esp.cs.columbia.edu

## Slide 14: ESP Architecture
Mix and match IP
Design and Reuse approach

## Slide 15: Tiny ASIC for Tiny ML on the edge
Processor:
Configures the accelerator
Pre-processing the inputs
Post processes and validates the accelerator performance
No floating point unit
Programmable
Accelerator: DNN for anomaly detection
Bad recreation = Anamoly
Memory:
SRAMs
Register files
1.2 mm2 ASIC in 22 FDSOI
Entirely digital: Compact
Low power: Reduce Vdd < 0.5V
NoC: Network on chip
processor tile
ZeroRISCY RISCV processor (Ibex)
25KGE
ULP 0.5V standard cell
IO and auxiliary tile
Debug unit & SPI
memory tile
Memory
200KB memory
DP ultra-low power
accelerator tile
DNN Accelerator
designed with hls4ml
for TinyMLPerf app
off-chip host

## Slide 16: Status
Chip is currently being tested
Investigated open source IP, tools and platforms
Established a path towards programmable data processing and verifying the hardware-software interface
Generic – yet specific to extreme environment operation

## Slide 17: Step 4: Can we make it more energy efficient? Neuromorphic, Analog and Beyond CMOS

## Slide 18: Pixel detector for phase III upgrades
Goals for scientific discovery
Data filtering by determining track momentum on-chip
Create hierarchical network and enable parallel computation.
System level constraints
Novel Device Development Highly Granular Sensors capable of producing both precise timing as well as charge information
New Machine learning algorithms for data processing (feature extraction and fast Inference)
Frontend Signal processing
Backend Data processing
Pixel level solution
Top level Architecture
ROIC

## Slide 19: Physics informed algorithm development
There is a strong correlation between the cluster shape/size and the location within a module
Low momentum positive tracks increase cluster size
Low momentum negative tracks decrease cluster size
Filtering: Developing an algorithm to classify clusters – TRANSMIT or DISREGARD:
3x to 80x data compression?
M. Swartz, JHU

## Slide 20: Hardware options: Proposed ML implementation
Neuron
Neuron
Neuron
Neuron
Neuron
Neuron
On-chip feature classification using DNN
ADC
On-chip feature classification using DNN
ADC
ADC
Digital neuromorphic implementation
Analog – Mixed Signal implementation using floating gates or memristive cross-bar arrays
Sensor (Preamp)
Sensor (Preamp)
Sensor (Preamp)
Sensor (Preamp)
Sensor (Preamp)
Sensor (Preamp)
Sensor (Preamp)
Sensor (Preamp)
Sensor (Preamp)
Sensor (Preamp)
Sensor (Preamp)
Sensor (Preamp)
Further compressive layers

## Slide 21: Frontend – Modified DVS pixel (Dynamic Vision System)
Low power and area pixel architecture ( DVS systems in 65 nm process of 9 × 9 µm2 to 18 × 18 µm2 have been demonstrated). Will not change much in 28 nm process
Creates a pulse train ( 2-5ns) dependent on the total charge in the pixel (spikes)
Large signals produce closely spaced spikes, small signal produce fewer farther spaced spikes
A negative pulse can dynamically reset the pixel (or can continue)
Information is time encoded in the pulse train
Non-uniformity correction and per pixel trimming can be handled by weight pruning (reusing resources)

## Slide 22: Neuromorphic approaches: digital spiking neural network
Local neighborhood for 1st stage of classification
  Compute total energy and track angle by spatio-temporal correlation
Mature systems are based on these SNNs e.g. Loihi, True-North, Spinnakar (in adv geometry nodes 14 nm and below)
Low–power since it runs without a clock
HL- LHC case: since events are uncorrelated between bunches we don’t need a complex network requiring historic information

## Slide 23: Converting raw data to local information
Use Neural Network as a classifier
Determine 3D position (finer than pixel size)
Total charge
Angular momentum
Timing information
Early decision: KEEP / DISCARD Determine if cluster has useful information

## Slide 24: Vector Matrix Multiplication
Basic building block of neural network
Analog implementation
Small footprint, programmable, large resistors
D. Strukov, UCSB

## Slide 25: Integrate a Field programmable Analog Array (FPAA)
Programmable Floating gate transistors for weights and switches
Structures are available in standard CMOS process (have been demonstrated in 350 nm to 40 nm nodes)
Radiation performance – unknown
Uses operation transconductance amplifier (OTA) with floating gates for Vector Matrix multiplication
Reconfigurable architecture by using a switch matrix and Manhattan routing to define interconnections
J. Hasler, Georgia Tech

## Slide 26: Use the pixel area for starting the classification process
Group 4 pixels together and share their analog well (similar to RD53)
Create computational analog blocks which gathers information from nearest 8/15 neighbors
CAB based on a TIA (FG or analog memristor)
Create hierarchical network.
Local physics information is important to determine track properties
Energy is shared within small area, which contains the angular information
CAB
CAB
CAB
CAB

## Slide 27: Memristive cross-bar arrays
D. Strukov, UCSB
Use of programmable resistors ( 1 – 10 GΩ
Small footprints ( < 1µm2)

## Slide 28: What’s next? Long term plans and impact beyond HEP

## Slide 29: PHYSICS driven: sensor, microelectronics and algorithm development

## Slide 30: Design Goals for the next 20 years: Enable Smart Sensors
Low power, low noise, ultra-sensitive analog for sensor signals (both amplitude and time)
SOC approach for integrated digital (reconfigurable, reprogrammable architectures)
AI-on-chip for compact ML inference models for edge compute (data processing at source)
Wireless / Integrated photonics (long distance data transfer)
Integrated THz electronics (short distance communication)

## Slide 31: HEP experiments are equivalent to real life applications
Benchmarks set by HEP experiments are beyond the current needs of industry applications
Mid-scale prototyping for HEP experiments advance lab to fab innovation required for growth in semiconductor manufacturing

## Slide 32: Acknowledgements
On behalf of several collaborators
Fermilab: Nhan Tran, Jim Hirschauer, Davide Braga, Doug Berry, Ron Lipton, Jennet Dickinson, Gauri Pradhan, Ben Parpillon, Christian Herwig
Northwestern University: Seda Memik, Manuel Blanco Valentin
Columbia University: Giuseppe Di Guglielmo, Davide Giri, Maico Cassel Santos, Luca Carloni
UIC: Corrinne Mills, Jieun Yoo, Amit Trivedi
JHU: Morris Swartz
and many others